## Slide 1: Tea Kettle Whimsy Fest 2014

## Slide 2: Everybody’s Working for the Weekend
Baseline Energy Use:
Weekday: 1.38 kWh
Weekend: 0.46 kWh
Annual: 439.6 kWh
Notes: Like an efficient refrigerator.

## Slide 3: This poor tea-kettle has no idea what’s about to happen.
Thermal imaging showed significant temperature loss

## Slide 4: A villain appears
Little known fact: tea-kettles love pizza.

## Slide 5: “I’ve become a monster!”

## Slide 6: “This ain’t so bad”

## Slide 7: Better, Stronger, Faster
Out-of-box heat loss rate: .7097 W/F
Insulated heat loss rate: .5847 W/F
Determined using highly sophisticated equipment.

## Slide 8: Weekday Modelling Assumptions
There is a 50% chance standby mode will be left on overnight.
Ecotope employees drink 12 oz of hot beverages at a time.
Ecotope employees use the tea kettle more in the morning then taper off throughout the day (much like a log-normal distribution).
There is a 50% chance the tea kettle will be reheated regardless of current temperature.
If there is less than 12 oz of water in the kettle someone will fill and boil it.

## Slide 9: Monte-Carlo Simulation results
Uninsulated tea-kettle:
  With standby option, uses 326.5 kWh/yr from weekdays
  Without standby option, uses 300.8 kWh/yr from weekdays
Fabulous tea-kettle:
  With standby option, uses 295.1 kWh/yr from weekdays
  Without standby option, uses 259.6 kWh/yr from weekdays
Switching from an uninsulated tea-kettle with standby to an insulated tea-kettle without standby lowers Ecotope’s EUI by .085, 0.11 if we scale to account for weekend use.

## Slide 10: Standby Mode, Am I Right?
If an uninsulated tea kettle is left alone for 30 minutes after boiling:
  With standby mode active it will take 1:35 minutes to re-boil from 179 (F)
  With standby mode off it will take 2:00 minutes to re-boil from 169 (F)
If an insulated tea kettle is left alone for 30 minutes after boiling:
  With standby mode active it will take 1:15 minutes to re-boil from 186 (F)
  With standby mode off it will take 1:45 minutes to re-boil from 175 (F)